Problems of the Front-end Electronics

Low Voltage Power Supply in CMS

# I. Vankov

## CMS – BARELL + 2 ENDCAPS

SUBDETECTORS:

- TRACKER (TR);

- ELECTROMAGNETIC CALORIMETER (ECAL);

- HADRON CALORIMETER (HCAL);

- MUON CHAMBERS (MU).

### NUMEROUS MEASURING CHANNELS:

- EMU – 483830;

- ECAL – 236830;

- CMS > 106.

POWER CONSUMING FRONT-END ELECTRONICS

Table 1

| SUBDETECTOR | DIGITAL I, kA | ANALOG I, kA | TOTAL POWER P, kW |
| --- | --- | --- | --- |
| ECAL | 13,7 | 7,2 | 92,5 |
| HCAL | 2,35 | 1,7 | 21,6 |
| EMU* | 3,7 | 2,6 | 43 |

*EMU – Endcap Muon Chambers

CLASSICAL SOLUTION – POWER SUPPLY CLOSE TO       THE LOAD

#### CMS LIMITATION FACTORS

- MAGNETIC FIELD

- RADIATION

##### MAGN. FIELD		        RADIATION

## INSIDE CMS			4 T		      2 Mrad	 5x1013 n/cm2

## CMS PERIPHERY	   0,1 – 0,32 T	    	    1,5/3x1010 n/cm2

## GALLERY		       0,05 T				      100 rad

## OUTSIDE CAVERN	  0					0

## TWO BASIC SOLUTIONS

## TWO STAGES LOW VOLTAGE SYSTEM

## THREE STAGES LOW VOLTAGE SYSTEM

## TWO STAGES LOW VOLTAGE SYSTEM

## FOR ECAL AND TRACKER (?)

## 1864 LV CHANNELS

4 VOLTAGES IN ONE CHANNEL:  +5, -2 – analog

+5, +2 – digital

HUGE POWER LOSS!

| ULOAD, V | ULVPS, V | (U, V | I, kA | (P, kW |
| --- | --- | --- | --- | --- |
| +5 | +11,9 | 5,9 | 11,9 | 70,2 |
| -2 | -5 | 3 | 1,9 | 5,7 |
| +5 | +8,3 | 3,3 | 2,3 | 7,6 |
| +2 | +5,8 | 3,8 | 5,0 | 19,0 |

Table 2

Total    102,5

102,5 kW > 92,5 kW

IF 120 m AWG 2 – 169,5 mm2 instead of 8 mm2 CABLE

2,2 kW instead of 47,6 kW

## BUT

CABLE WEIGHT 176 900 KG

CABLE CROSS-SECTION AREA 6320 cm2 (80X80 cm)

CABLE PRICE 1 726 000 $

THREE STAGES LOW VOLTAGE SYSTEM

## FOR EMU and HCAL

VICOR DC-DC CONVERTERS

## 300 V input,  5 – 12 V output (nominal)

## ME1/1 LOW VOLTAGE SYSTEM

Fig. 3

FOR ONE ENDCAP

30 kW input power at 300 V (70% efficiency) -

100 A current trough the 100 m long cables

AWG – 2  -  VOLTAGE DROP – 1,5 V

- POWER LOSS         - 144 W

MAGNETIC FIELD SHIELDING FOR DC-DC CONVERTORS

FERMILAB’S PROTOTYPE - 1,25 cm SOFT IRON PLATES

WITH WATER COOLING

Fig. 4

RADIATION PROBLEMS

TESTS WITH LOW ENERGY NEUTRONS:

OPTO COUPLER REPLACING BY HEWLETT-PACKARD’S

DEVICE

NEUTRON ENERGY – 60 – 200 MEV – SINGLE EVENT EFFECTS

TEST – 60 MeV PROTON BEAM IN Louven-la-Neuve, Belgium:

V300B12C250AL, VIN=300V,  VOUT= 12V, IOUT=21A

TESTED AT, VIN=200V,  VOUT=7,5V, IOUT=20 A

## V300B5C200A, VIN=300V, VOUT=5V, IOUT =40 A

## TESTED AT VIN=200V, VOUT=5,2V, IOUT=25 A

PASSED 2x1011 protons/cm2 WITHOUT PROBLEMS.

CONCLUSION

VICOR DC-DC CONVERTERS ROBUST AT REDUCED INPUT VOLTAGE – 200 V AND REDUCED OUTPUT POWER

PRICE OF EMU LVS SECOND STAGE:

- DC-DC CONVERTERS  – 150 k$

(with filters and PCB)

- MAGNETIC SHIELDING –70 k$

TOTAL	  220 k$

TRANSFORMER SOLUTION FOR SECOND STAGE:

400 Hz AC

FULL WAVE RECTIFIER

PROVISORY COST ESTIMATION:

- 100 kVA 400 Hz MOTOR-GENERATOR    - 30 k$

- TRANSFORMERS					    - 15 k$

- RECTIFIERS AND FILTERS			    -   8 k$

## TOTAL	       53 k$

LINEAR VOLTAGE REGULATORS

## EMU and HCAL - LHC4913

TESTS:

- SPURIOUS CURRENT IN LOW VOLTAGE CONDITION;

- NOT OPERATING INHIBIT FUNCTION

- INSUFICIENT OUTPUT CURRENT - IOUT ( 2,6 A (INOM=3 A)

## ECAL – MOTOROLA MC1723CP REGULATOR + SIEMENS

## SIPMOS TRANSISTOR SPP30N03L

ALL CONTROL FUNCTIONS IN FIRST STAGE

TEST – ON PSI OPTIS BEAM with 1,25x109 protons/cm2s

of 64 MeV

GENERAL CONCLUSIONS

- The comparisons between three described variants of LVS show clearly, that the best solution is the three-stage system with transformers in second stage. Only reason to abandon it could be safety or noise considerations.

- Further investigations and efforts needed for application of this system in ECAL and TRACKER.

- Improvement of LHC4913 and further investigations of commercial low voltage regulators are necessary for finding and optimal solution.

# Text boxes

8 m

120 m

###### Fig. 1

###### LOAD

###### LVR

## LVPS

4(12 m

4(12 m

4(12 m

Fig. 2

100 m

300 V

# CSC FE

boards

# CSC FE

boards

# CSC FE

boards

# LVDB

# LVDB

# LVDB

# DC-DC

# DC-DC

# DC-DC

3 (

# AC-DC

7 V

6 V

6 V

7 V

6 V

7 V

### Fig. 3

2,4

m

2m

=0,2 m

l

+3.3V(0.75A)

+6.0V(0.75A)

+5.0V(0.75A)

CFEB

+3.3V(0.75A)

+6.0V(0.75A)

+5.0V(0.75A)

CFEB

+3.3V(0.75A)

+6.0V(0.75A)

+5.0V(0.75A)

CFEB

+3.3V(0.75A)

+6.0V(0.75A)

+5.0V(0.75A)

CFEB

+3.3V(0.75A)

+6.0V(0.75A)

+5.0V(0.75A)

CFEB

+3.3V(0.75A)

+6.0V(0.75A)

+5.0V(0.75A)

CFEB

LVDB

+3.3V(0.75A)

+6.0V(0.75A)

+5.0V(0.75A)

CFEB

+5.5V(0,1A)

=1,5 m

l

AFEB

+5.5V(0,1A)

=1,5 m

l

AFEB

+5.5V(0,1A)

=1,5 m

l

AFEB

+5.5V(0,1A)

=1,5 m

l

AFEB

+5.5V(0,1A)

=1,5 m

l

AFEB

+5.5V(0,1A)

=1,5 m

l

AFEB

=0,65 m

l

=0,45 m

l

=0,45 m

l

=0,65 m

l

=0,65 m

l

=0,45 m

l

=0,45 m

l

+5.5V(2.5A)

+3.3V(1.5A)

+2.5V(0.5A)

ALCT

for DC-DC converters

Soft Iron Box

+7.0V(16A)

+6.0V(26A)

YE1

Panel

Patch

10

m

10

m